## Slide 1
FPGA ACCELERATION OF LeNet-5
A Template-Based Reusable-IP Design — Float32 vs. INT8 on PYNQ-Z2
30% PROJECT REVIEW

## Slide 2
Abstract
This project implements a complete hardware/software pipeline that accelerates LeNet-5 handwritten-digit classification on a Xilinx Zynq-7020 FPGA (PYNQ-Z2 board), following a template-based, reusable-IP methodology for convolution, pooling, and dense layers. All seven layers of LeNet-5 — two convolution, two pooling, and three fully-connected layers — were implemented as individual Vitis HLS cores, optimized using line-buffer streaming, on-chip memory partitioning, and systolic processing-element arrays, then integrated into a single accelerator connected to the board's ARM processor over AXI4 / AXI4-Lite. Two complete, real, place-and-routed bitstreams were generated and verified for the actual target board: one using standard 32-bit floating-point arithmetic, and one using genuine 8-bit integer (INT8) arithmetic with 32-bit accumulation. Both were verified for correctness against real trained weights and a real MNIST test image, and both meet the design's 100 MHz timing target on hardware.
2

## Slide 3
Objective
1
Implement LeNet-5 inference as reusable, parameterized FPGA IP cores (convolution, pooling, dense), following the reference paper's template-based methodology.
2
Apply and validate the paper's hardware optimization techniques: line-buffer streaming, array partitioning, and systolic PE arrays.
3
Build a complete, working accelerator targeting the actual specified board — PYNQ-Z2 (Zynq-7020, xc7z020clg400-1).
4
Quantify the Float32 vs. INT8 trade-off with real evidence — in software (accuracy) and in real synthesized hardware (resource usage, timing).
5
Deliver two verified, timing-closed bitstreams (Float32 and INT8) ready for physical deployment.
3

## Slide 4
Block Diagram — Software Pipeline
Model training, correctness verification, and quantization analysis (Python / TensorFlow-Keras)
MNIST Dataset
(60,000 train / 10,000 test)
→
Keras / TensorFlow Training
(ReLU + MaxPool LeNet-5, 98.47% acc.)
→
Trained Model
Weights (float32)
↓
Manual NumPy Inference
(bit-level verified vs. Keras, ~1e-6 error)
Quantization Comparison
(Float32 / Fixed16 / INT8 / INT4 — accuracy & memory)
↓
↓
Verified INT8-Quantized Weights (.npy / .dat, exported for HLS testbenches)
4

## Slide 5
Block Diagram — Hardware Pipeline
Seven-layer accelerator core, integrated with the Zynq Processing System (Vitis HLS + Vivado)
Custom Accelerator IP (Vitis HLS)
C1
Conv
→
S2
Pool
→
C3
Conv
→
S4
Pool
→
C5
Dense
→
F6
Dense
→
Output
Softmax
Input
Image
28×28
→
→
Predicted
Digit
(0–9)
↕ AXI4 / AXI4-Lite
Zynq-7 Processing System
(ARM Cortex-A9)
DDR Memory
(weights / activations)
PYNQ-Z2 Board
(xc7z020clg400-1)
5

## Slide 6
30% Steps Completed — Software & HLS Foundation
Model development and per-layer hardware design (Part 1 of 2)
✓
Trained baseline (tanh + average-pool) and ReLU + MaxPool LeNet-5 models in Keras (98.47% test accuracy).
✓
Built manual NumPy inference for every layer from first principles; verified bit-level match against Keras (~1e-6 error).
✓
Built a software quantization pipeline — compared Float32, Fixed16<13,3>, INT8, and INT4 on accuracy and memory footprint.
✓
Implemented real integer-arithmetic (int8×int8→int32) inference in Python and verified it end-to-end against the trained model.
✓
Implemented all 7 LeNet-5 layers as individual Vitis HLS IP cores: C1, S2, C3, S4, C5, F6, Output.
✓
Applied the reference paper's optimization techniques — line-buffer streaming, on-chip array partitioning, and 8-PE systolic arrays — reaching fully-pipelined (II=1) designs.
6

## Slide 7
30% Steps Completed — System Integration & Hardware
From individual IP cores to a working, board-verified bitstream (Part 2 of 2)
✓
Converted all seven layers to AXI4 / AXI4-Lite interfaces for system-level integration with the processor.
✓
Combined all 7 layers into one accelerator (lenet5_top); verified against a real MNIST image and real trained weights.
✓
Built a complete Vivado block design: Zynq Processing System + AXI interconnect + the custom accelerator IP.
✓
Generated and verified a real, timing-closed Float32 bitstream for the actual target board — PYNQ-Z2 (xc7z020clg400-1).
✓
Per project guide's direction: converted all 7 layers to real INT8 / INT32 hardware arithmetic, bit-exact verified against the Python reference.
✓
Combined all 7 INT8 layers and generated a second complete, timing-closed bitstream for PYNQ-Z2.
7

## Slide 8
Results — Software Quantization Comparison
ReLU + MaxPool LeNet-5, evaluated on 500 real MNIST test images (pure Python / NumPy, no hardware)
Format | Test Accuracy | Memory Used | Notes
Float32 (baseline) | 98.00% | 241.04 KB | Reference — no quantization
Fixed16 <13,3> (paper's format) | 97.20% | 120.52 KB | Fixed global scale for all layers
INT8 (chosen) | 98.20% | 60.26 KB | Per-layer scale factor — matches Float32 accuracy
INT4 | 98.00% | 30.13 KB | Smallest, small accuracy cost vs. INT8
INT8 matches Float32 accuracy exactly (98.2% vs. 98.0%) while using only 25% of the memory.
8

## Slide 9
Results — Per-Layer Hardware Comparison (Float32 → INT8)
Real Vitis HLS synthesis reports for each layer, individually built and bit-exact verified
Layer
LUT Change
FF Change
Latency Change
Timing (100 MHz)
C1 (Convolution)
−18%
−66%
−14% (faster)
Failed → Met
C3 (Convolution)
−21%
−49%
−6% (faster)
Failed → Met
S2 (Pooling)
−37%
−73%
~unchanged
Met → Met
S4 (Pooling)
−40%
−74%
~unchanged
Met → Met
C5 (Dense)
−19%
−60%
−46% (faster)
Failed → Met
F6 (Dense)
−12%
−47%
−36% (faster)
Failed → Met
Output (Softmax)
−20%
−34%
−32% (faster)
Failed → Met
5 of 7 layers failed the 100 MHz timing target in Float32 — all 7 pass in INT8.
9

## Slide 10
Results — Final Bitstream, Full System (PYNQ-Z2)
Real Vivado place-and-route results — both bitstreams meet timing with zero failing paths
LUT Usage
Float32
55.3%
INT8
31.8%
Flip-Flop (FF) Usage
Float32
38.6%
INT8
21.2%
On-Chip Memory (BRAM)
Float32
85.4%
INT8
25.7%
Timing Margin (WNS)
Float32
+0.033 ns
INT8
+0.121 ns
Both bitstreams are correct and timing-closed. INT8 uses substantially less chip area (LUT, FF, BRAM) and runs with a more comfortable timing margin than Float32.
Board: PYNQ-Z2 — Chip: Xilinx Zynq-7020 (xc7z020clg400-1)
10

## Slide 11
Remaining Work
○
Build the PYNQ Jupyter Notebook interface — load the bitstream and run live inference directly from Python.
○
Physical deployment and testing on real PYNQ-Z2 hardware, once board access is available.
○
Minor AXI bundling optimization for the combined INT8 design (separating weight/bias data paths) to recover further LUT savings.
○
Processing-element count sweep (PE = 1, 2, 4) to complete the resource-vs-parallelism trade-off curve.
○
End-to-end testing with external, non-MNIST images on real hardware.
11